## Slide 1: From last class: Selectivity vs Specificity

## Slide 4: Fluorescence Advantage
Fluorescence is measured over a dark background, while absorbance is measured over a bright background.
Measuring signal over a large background is hard.
Chemical noise/background is a major limitation.

## Slide 5: Quantitative Analysis 101
What does it mean to be quantitative?

## Slide 6: The change in signal should reflect the change in quantity

## Slide 7: Quantitative Analysis 101
Amount (moles)
Measured Intensity (Area)
LOD
LLOQ
ULOQ
Linear Dynamic Range
LOD: Limit of Detection
LLOQ: Lower Limit of Quantitation
ULOQ: Upper Limit of Quantitation

## Slide 8: Quantitative Analysis 101: Using an Internal Std
Amount (moles)
Intensity Ratio (Area Ratio)
LOD
LLOQ
ULOQ
Linear Dynamic Range
LOD: Limit of Detection
LLOQ: Lower Limit of Quantitation
ULOQ: Upper Limit of Quantitation

## Slide 9: Quantitative Analysis 101
What does it mean to be quantitative?
What does signal calibration mean?

## Slide 10: Measurements on different platforms are not measured on the same scale

## Slide 11: Between Batch/Platform/Lab Signal Calibration
Purpose of signal calibration
Placing signal on the same scale
Often the scale is arbitrary
  Kilogram = mass of a liter of water at freezing point
  Meter = 1/10,000,000 the distance from the equator to the north pole
  Pee dee belomnite (PDB) = reference for 13C, fossil found in Peedee Formation in South Carolina
  Standard mean ocean water (SMOW) = reference for 18O, arbitrary mix of distilled water from different regions of the world.

## Slide 12: What you calibrate against is important

## Slide 13: What you calibrate against is important
Bicinchoninic acid (BCA) is the current standard for measuring protein abundance.

## Slide 14: What you calibrate against is important
Smith et al., Anal Biochem 1985

## Slide 15: What is the difference between relative and absolute quantitation?

## Slide 16: Major Quantitative Figures of Merit
LOD – Limit of Detection
LOQ – Limit of Quantitation
Precision
  Within batch/day
  Between batch/day

## Slide 17: Limit of detection
Is a signal statistically different from a blank?

## Slide 18: Limit of Quantitation
Does the change in quantity reflect the change in signal?