## Slide 1: Light Sources
Genome 575: Fundamentals of Biomedical Instrumentation
Brian Beliveau

## Slide 2
Recap from the first module
There are many questions to ask about data
Continuous information can be evaluated or thresholded
Discrete information can be binarized around threshold values
The performance of a given threshold choice can be evaluated with ROC curves

## Slide 3
The competition…
https://dnm.nflximg.net/api/v6/2DuQlx0fM4wd1nzqm5BFBi6ILa8/AAAAQYwP3BYZ2Ri_-P-sY4_vtR9_fv6KPptWKKniY2_VxxOzqurvjAbe7bi4XPq2NbcH4vw99f1gFDyU_TZe7bkeHOBKNYccZkoFBoRsCHFtqWFtHPYk16RT26YMxUs8PffGpvROrvismA_Kt8PHRAuviZLp.jpg?r=b5e
2022
2023

## Slide 4
2024
https://vimeo.com/blog/post/video-deepfakes/

## Slide 5
2025
https://vimeo.com/blog/post/video-deepfakes/

## Slide 6
Returning to information…
How are these different?
Wikipedia

## Slide 7
Barcode information content
UPC-A barcode
Wikipedia
95 black/white modules (bits of infomration)
Up to 12 positions, 0–9 value at each
10^12 possibilities
V4 QR code (33x33)
1089 black/white modules (bits of information)
Digits, characters, symbolic character encodings
Up to 114 alphanumeric characters 45^144 = 10^187 possibilities
10e+80 atoms
in the known
universe!

## Slide 8
Discussion point
What is the most surprising thing you’ve learned in the class so far?
https://images.emojiterra.com/google/android-11/512px/1f914.png

## Slide 9
Let’s talk about (visible) light
https://www.thoughtco.com/thmb/jEWJTLUBQRRgWgmKng6JPuX5E0M=/2180x1400/filters:fill(auto,1)/90191671-56a1322a3df78cf772684fbf.jpg
What is light?
Where does it come from?

## Slide 10
Sunlight
https://media.npr.org/assets/img/2020/04/17/gettyimages-102853378_custom-322a77f3aa92129f4a84f4d2dd98ac2ca1a078b8-s1100-c50.jpg
What is the source of visible sunlight?

## Slide 11
Black body radiation
https://upload.wikimedia.org/wikipedia/commons/thumb/d/d8/Black_body_realization.svg/1920px-Black_body_realization.svg.png, https://upload.wikimedia.org/wikipedia/commons/thumb/e/e9/Color_temperature_black_body_800-12200K.svg/1024px-Color_temperature_black_body_800-12200K.svg.png, https://upload.wikimedia.org/wikipedia/commons/thumb/1/19/Black_body.svg/606px-Black_body.svg.png
Radiation emitted by all matter above 0 K due to thermal motion of elementary particles (e-, p+)
“Black body”: isolated system in thermal equilibrium
E = hf (Planck’s constant originated by quantizing changes in black body radiation as a function of f)

## Slide 12
Black body radiation and the sun
https://upload.wikimedia.org/wikipedia/commons/thumb/7/76/Sun_diagram.svg/500px-Sun_diagram.svg.png , https://media.npr.org/assets/img/2020/04/17/gettyimages-102853378_custom-322a77f3aa92129f4a84f4d2dd98ac2ca1a078b8-s1100-c50.jpg, svg.png, https://upload.wikimedia.org/wikipedia/commons/thumb/e/e9/Color_temperature_black_body_800-12200K.svg/1024px-Color_temperature_black_body_800-12200K.svg.png
EM radiation from the sun matches closest to black body radiation with T = ~5800K
EM radiation from sun is emitted from the photosphere (4 in diagram above), which has a T of ~5800k

## Slide 13
Incandescent lights
https://upload.wikimedia.org/wikipedia/commons/thumb/b/b4/Gluehlampe_01_KMJ.png/340px-Gluehlampe_01_KMJ.png, https://upload.wikimedia.org/wikipedia/commons/1/17/Tungsten_filament.JPG, https://upload.wikimedia.org/wikipedia/commons/b/be/Spectral_power_distribution_of_a_25_W_incandescent_light_bulb.png
Electric current used to heat a filament -> thermal radiation
Inefficient: most energy lost as heat (5% goes to visible light)

## Slide 14
Fluorescent lights
https://upload.wikimedia.org/wikipedia/commons/thumb/5/5b/Leuchtstofflampen-chtaube050409.jpg/1920px-Leuchtstofflampen-chtaube050409.jpg, https://upload.wikimedia.org/wikipedia/commons/8/8e/Germicidal_UV_discharge_tube_glow.jpg https://upload.wikimedia.org/wikipedia/commons/thumb/5/53/Jablonski_Diagram_of_Fluorescence_Only-en.svg/1024px-Jablonski_Diagram_of_Fluorescence_Only-en.svg.png
An ionized (ie, plasma) mix of Hg and inert gas sealed
Electrical discharge sent through bulb, electrons collide with Hg
Collisions -> UV photons -> collision with surface coating -> vis photons
Jablonski diagram

## Slide 15
What makes a good light source?
Brightness
Wavelength availability
Spectral bands
Dispersion
Collimation
Stability
Modulation/control
Lifetime
Cost
Engineering concerns (e.g. cooling, noise)
Safety
Durability

## Slide 16
HBO “Burner” lamps
https://zeiss-campus.magnet.fsu.edu/articles/lightsources/images/mercurylampsfigure2.jpg, https://zeiss-campus.magnet.fsu.edu/articles/lightsources/images/mercurylampsfigure1.jpg
Specialized version of fluorescent lights using Hg
Useful bands of intensity for common fluorescent labels
Do not last super long; break easily

## Slide 17
Metal halide lamps
https://zeiss-campus.magnet.fsu.edu/articles/lightsources/images/metalhalidelampsfigure1.jpg
Similar to HBO in mechanism of action
Better coverage of “dip” in blue/green part of spectrum
Longer lasting than HBO (have largely replaced)

## Slide 18
LEDs
https://zeiss-campus.magnet.fsu.edu/articles/lightsources/images/ledsfigure4.jpg, https://zeiss-campus.magnet.fsu.edu/articles/lightsources/images/ledsfigure2.jpg
Semi-conductor driven excitation/relaxation of e- over defined ‘band gaps’
Possible to precisely tune 𝝀, generate high power
Single wavelength and white light options
Extremely durable. The new standard.

## Slide 19
Lasers
https://en.wikipedia.org/wiki/File:Lasers.JPG, https://en.wikipedia.org/wiki/File:Laser.svg
LASER = “Light Amplification by Stimulated Emission of Radiation”
More accurately: LOSER / “Light Oscillation by Stimulated Emission of Radiation”
As name suggests, works via stimulated emission

## Slide 20
Stimulated Emission
https://en.wikipedia.org/wiki/File:Stimulated_Emission.svg, https://upload.wikimedia.org/wikipedia/commons/thumb/9/92/Lasercons.svg/466px-Lasercons.svg.png
Initial excitation events driven by spontaneous emission
Collisions between incident photons and excited gain medium lead to stimulated emission events
Stimulated emission -> monochromatic, coherent light
Very high powers, “clean” point sources can be generated

## Slide 21
Properties of light: Reflection
https://upload.wikimedia.org/wikipedia/commons/e/e3/F%C3%A9nyvisszaver%C5%91d%C3%A9s.jpg, https://www.thorlabs.com/images/TabImages/Variable_Centering_Plate_A1-150.jpg
Mirror

## Slide 22
Properties of light: Refraction
https://upload.wikimedia.org/wikipedia/commons/8/85/Refraction_photo.png,
Lenses

## Slide 23
Properties of light: Absorption
https://www.edinst.com/wp-content/uploads/2019/08/BLL-2.jpg, https://www.thorlabs.com/images/TabImages/Variable_ND_Filter_A5-780.jpg
Filters

## Slide 24
Challenge: Power density “consultants”
https://hubner-photonics.com/wp-content/uploads/2020/05/Performance-data-beam-profile-04-01-Series.png
Your camera chip (white) and Gaussian laser beam profile are shown ->
Is this set-up ideal for quantitative imaging? Why or why not?
Given the assumptions below, calculate the power density of the cyan box in kW/cm^2. How does this compare to the intensity of the sun?
  The central white + purple area is roughly uniform in intensity at 100 mW
  The cyan box is 1024 x 1024 100 nm pixels
Devise an engineering solution to make the illumination intensity uniform over the white box

## Slide 25
Challenge: Power density “consultants”
https://hubner-photonics.com/wp-content/uploads/2020/05/Performance-data-beam-profile-04-01-Series.png
~1 kW/m^2 at surface