## Slide 1: From last class: Selectivity vs Sensitivity

## Slide 4: Fluorescence Advantage
Fluorescence is measured over a dark background, while absorbance is measured over a bright background.
Measuring signal over a large background is hard.
Chemical noise/background is a major limitation.

## Slide 5: Quantitative Analysis 101
What does it mean to be quantitative?

## Slide 6: The change in signal should reflect the change in quantity

## Slide 7: Quantitative Analysis 101
Amount (moles)
Measured Intensity (Area)
LOD
LLOQ
ULOQ
Linear Dynamic Range
LOD: Limit of Detection
LLOQ: Lower Limit of Quantitation
ULOQ: Upper Limit of Quantitation

## Slide 8: Quantitative Analysis 101: Using an Internal Std
Amount (moles)
Intensity Ratio (Area Ratio)
LOD
LLOQ
ULOQ
Linear Dynamic Range
LOD: Limit of Detection
LLOQ: Lower Limit of Quantitation
ULOQ: Upper Limit of Quantitation

## Slide 9: Quantitative Analysis 101
What does it mean to be quantitative?
What does signal calibration mean?

## Slide 10: Measurements on different platforms are not measured on the same scale

## Slide 11: Between Batch/Platform/Lab Signal Calibration
Purpose of signal calibration
Placing signal on the same scale
Often the scale is arbitrary
  Kilogram = mass of a liter of water at freezing point
  Meter = 1/10,000,000 the distance from the equator to the north pole
  Pee dee belomnite (PDB) = reference for 13C, fossil found in Peedee Formation in South Carolina
  Standard mean ocean water (SMOW) = reference for 18O, arbitrary mix of distilled water from different regions of the world.

## Slide 12: Use of calibration curve to convert signal to quantity
Analyte (m/z = M)
Where: ki= is the slope of the standard curve Ab  0 Area from a blank
Intensity
M
Intensity
time
m/z
A
Known Amount
Measured Signal (Area)

## Slide 13: Use of calibration curve to convert signal to quantity
Sample (m/z = M) Spiked with
Internal Standard (m/z = M+i)
Where: k0/i= is the slope of the standard curve Ri  0 Area ratio from a blank … only internal std
Intensity
M
M+ i
Intensity
time
m/z
R0 =
A0
Ai
n0
ni

Known Amount
Measured Signal (Area Ratio)

## Slide 14: What you calibrate against is important

## Slide 15: What you calibrate against is important
Bicinchoninic acid (BCA) is the current standard for measuring protein abundance.

## Slide 16: What you calibrate against is important
Smith et al., Anal Biochem 1985

## Slide 17: What is the difference between relative and absolute quantitation?

## Slide 18: What is the difference between a “differential” and a “quantitative” measurement?

## Slide 19: What does it mean if these are the two points?
Amount (moles)
Measured Intensity (Area)
LOD
LLOQ
ULOQ
Linear Dynamic Range
LOD: Limit of Detection
LLOQ: Lower Limit of Quantitation
ULOQ: Upper Limit of Quantitation

## Slide 20: Major Quantitative Figures of Merit
LOD – Limit of Detection
LLOQ – Limit of Quantitation
Precision
  Within batch/day
  Between batch/day

## Slide 21: Limit of detection
Is a signal statistically different from a blank?

## Slide 22: Limit of Quantitation
Does the change in quantity reflect the change in signal?
The limit of quantitation (LOQ; also referred to as the lower limit of the measuring interval (LLMI)) is defined by the Clinical and Laboratory Standards Institute as ″the lowest measurand concentration at which all defined performance characteristics of the measurement procedure are met.″
Our lab often chooses for LLOQ:
Must be >LOD
Must have a coefficient of variation <20% (aka S/N >5)

## Slide 23: Limit of Quantitation
Does the change in quantity reflect the change in signal?
The limit of quantitation (LOQ; also referred to as the lower limit of the measuring interval (LLMI)) is defined by the Clinical and Laboratory Standards Institute as ″the lowest measurand concentration at which all defined performance characteristics of the measurement procedure are met.″

## Slide 24: Questions:
Can a method be quantitative if you don’t know the range over which the signal reflects the quantity?
Design an approach to confirm linearity and LLOQ for peptides in a complex matrix?
  Assume you have < 50 analytes in your assay.
  Assume you have >1000 analytes in your assay?

## Slide 25: Matched Matrix Dilution Curves
Building on: Grant and Hoofnagle, Clin Chem 2014

## Slide 26: Matching the Matrix is Important

## Slide 27: Reference Yeast BY4742 Diluted in 15N Yeast (S288c)
Fractional Dilution
0
0.2
0.4
0.6
0.8
1
Peak area (1e9)
0
0.5
1
1.5
2
Protein SSA1 (2.69E+05 copies/cell)
Fractional Dilution
0
0.2
0.4
0.6
0.8
Peak area (1e7)
0
1.0
1.2
0.6
0.8
Protein LSM2 (2.21E+03 copies/cell)
0.2
0.4
Notes: Protein value = sum(peptides(sum(fragments))
function broken in post-3.4.0 MSstats builds, waiting to hear back from collaborator

## Slide 28: Not all Peptides are Equal Quantitative Proxies for a Protein
Notes: plasma membrane ATPase (PMA1

## Slide 29: Not all Peptides are Quantitative

## Slide 30: Method of Standard Addition
Can’t assess Limit of Quantification. Can only assess whether the sample us above the LOQ

## Slide 31: Mixing two samples of extreme conditions
Assume that you have a healthy and a disease cohort.
You can take a pool of the healthy and a pool of the disease to demonstrate that the measurement is linear between the two conditions
Example
  100% condition A
  80% condition A, 20% condition B
  50% condition A, 50% condition B
  20% condition A, 80% condition B
  100% condition B