## Slide 1: Genome 575: Fundamentals of Biomedical Instrumentation
Introductions
  Name
  Preferred pronouns
  Science you are interested in
  Where are you from
  Fun Fact
Purpose of the Class … how it came to be
An introduction to the fundamentals of instrumentation commonly used in biomedical research settings including mass spectrometers, biochemical separations, optical microscopes, and DNA sequencers. Emphasis on a practical understanding of the physical and chemical properties that underlie operation and sources of uncertainty, noise, and error.

## Slide 2: Website https://github.com/beliveau-lab/gen575

## Slide 3
Grades:
Participation: 60%
Problem sets: 40% (4, worth 10% each)
Details:
Absence is ok but please let us know about travel and known absences in advance. Communicate illness and emergencies ASAP.
Late homework will be accepted but penalized (10% per day)

## Slide 4: What you should expect
You should expect to be challenged!
  There should be material that you know but also there should be material that we present that you don’t know.
You should expect to have a better fundamental understanding of the principles that define many biomedical instruments
There will be some topics presented multiple times during the class in different contexts and different ways.
  You might even hear contradictory things from Mike/Brian
This year is the fourth time we have taught this class! There might be hiccups.

## Slide 5: What we expect
We expect you to participate!
  The more you participate the more we will all get out of the course.
  Don’t hesitate to ask a question. If you have a question, it is almost certain that someone else has it too. Interrupt us.
We want feedback and to hear if content isn’t working.
We expect you all to come from different scientific backgrounds and interests.
We expect to learn from you!

## Slide 6: Information Currencies
Genome 575: Fundamentals of Biomedical Instrumentation
Brian Beliveau

## Slide 7
Goals for this class
Think about instruments in new ways
  Dive deep
  New angles
Gain a better of understanding of what is being measured and how it can mislead you
https://www.istockphoto.com/photo/scuba-diving-in-the-wild-blue-yonder-in-french-polynesia-gm484092196-71525013
https://static1.srcdn.com/wordpress/wp-content/uploads/2020/11/tim-and-eric-mind-blown.jpg?q=50&fit=crop&w=960&h=500&dpr=1.5

## Slide 8
Le Systeme International d'Unites (SI)
Foundation of the metric system
Built on 7 base units + 7 associated constants. Assumed to be “mutually independent” (2019)
Many derived units
https://www.nist.gov/sites/default/files/styles/480_x_480_limit/public/images/2016/11/01/si-globe-logo.jpg?itok=9Z03oUtF

## Slide 9
A guided tour of the SI base units
https://media.istockphoto.com/photos/travel-to-europe-tourist-looking-at-map-on-the-street-summer-holidays-picture-id1020217050?k=20&m=1020217050&s=612x612&w=0&h=7ldikMFS5XidjVHwYMnMRnfhXrSdqA3WRdUKkLYelIw=

## Slide 10
Kilogram (kg) : a unit for massive calculations!
Measurable: Mass
  The quantity of matter in a physical body
  Inertial mass: resistance to changes in velocity
  Gravitational mass: defines strength of interaction with gravitational fields (weight)
Constant: h, 6.62607004 × 10-34 m2 kg / s
  Planck’s constant
  Energy = h * frequency
https://upload.wikimedia.org/wikipedia/commons/a/af/Watt_balance%2C_large_view.jpg
Kibble Balance

## Slide 11
Meter (m) : a unit for lengthy journeys!
Measurable: Length
  A measure of distance in a dimension
Constant: c, 299,792,458 m / s
  Speed of light in a vacuum
  s defined based on the Cesium standard (more soon!)
https://www.google.com/url?sa=i&url=https%3A%2F%2Fstarwars.fandom.com%2Fwiki%2FLightspeed%2FLegends&psig=AOvVaw2JW1S6KFHyEllGYWRdSznb&ust=1648597525352000&source=images&cd=vfe&ved=0CAsQjRxqFwoTCIiJgdL-6fYCFQAAAAAdAAAAABAD

## Slide 12
Second (s) : a unit for timeless experiences!
Measurable: Time
  A measure of duration
Constant: ∆νCs, 9,192,631,770 s-1
  A measure of the frequency of the relaxation of Cs133 (Spin F = 4) to Cs133 (F = 3)
https://upload.wikimedia.org/wikipedia/commons/4/43/NIST-F2_cesium_fountain_atomic_clock.jpg
“Atomic clock”

## Slide 13
Ampere (A) : a unit for shocking discoveries!
Measurable: Electric current
  A measure of charge flow through a conductor or space
Constant: e, 1.602176634 × 10-19 coulombs
  Elementary charge (proton+ / electron-)
  1 coulomb = 1 A * 1 s
  The value of e depends on h (via Ohm’s law V = IR and measures of V, R), ∆νCs
https://www.nist.gov/sites/default/files/styles/960_x_960_limit/public/images/2017/08/31/JJ-9550x-60deg_002_colored.jpg?itok=SKo9MpkM
Josephson junction (measures V)

## Slide 14
Kelvin (K) : a unit for heartwarming events!
Measurable: Temperature
  A measure of thermal energy
Constant: k, 1.380649×10−23 J / K
  Boltzmann constant
  1 joule (J) = 1 (kg * m2) / s2
  k was measured empirically using an “acoustic resonator”
https://www.nist.gov/sites/default/files/styles/960_x_960_limit/public/images/2017/12/20/mike_and_gas_constant_resonator_img002_resized.jpg?itok=N4xGI-nI

## Slide 15
Mole (mol) : a unit for numerous possibilities!
Measurable: Amount of substance
  A measure of how many elementary entities of a given substance are in an object/sample
Constant: NA, 6. 02214076 x 1023 particles / mol
  Avogadro’s number
  Value set by the International Bureau of Weights and Measures
https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.istockphoto.com%2Fphotos%2Fmole-animal&psig=AOvVaw3-kGEh5rmx2g4bcchmx9k_&ust=1648749197129000&source=images&cd=vfe&ved=0CAsQjRxqFwoTCMDImcWz7vYCFQAAAAAdAAAAABAD

## Slide 16
Candela (cd) : a unit for illuminating analyses!
Measurable: Luminous intensity
  A measure of luminous power per unit solid angle (ie, some FOV) emitted by a point light source
Constant: Kcd, 683 lumens / W
  Based on the luminous efficacy of monochromatic radiation of frequency 540 × 1012 Hz (~555 nm)
  FWIW in optics we just use W
https://www.ksoc.co.jp/en/seihin/lasers/img/dpss.jpg

## Slide 17
Can’t get enough of the SI constants?
https://www.nist.gov/sites/default/files/styles/960_x_960_limit/public/images/2018/10/30/17pml015_si-constants-card.jpg?itok=Ecezgy_j

## Slide 18
Electromagnetic radiation
https://science.nasa.gov/files/science-pink/s3fs-public/styles/science_news_hero_image/public/thumbnails/image/intro-1.jpg?itok=iRsuB2Q7
What is your favorite part of the EM spectrum?

## Slide 19
Electromagnetic radiation
https://science.nasa.gov/files/science-pink/s3fs-public/styles/science_news_hero_image/public/thumbnails/image/intro-1.jpg?itok=iRsuB2Q7
Wavelength (𝝀) = c (velocity) / frequency (f)
Greater f == more energy

## Slide 20
https://i.redd.it/pz6s3irlge861.png
What is going on here?

## Slide 21
Wave-particle duality
https://i.redd.it/pz6s3irlge861.png, https://upload.wikimedia.org/wikipedia/commons/thumb/3/39/Young%27s_slits.jpg/2880px-Young%27s_slits.jpg, https://static1.srcdn.com/wordpress/wp-content/uploads/2020/11/tim-and-eric-mind-blown.jpg?q=50&fit=crop&w=960&h=500&dpr=1.5
Light waves interfere with each other -> diffraction pattern
Place a detector at a slit, diffraction pattern disappears (!!)
Electromagnetic radiation behaves simultaneously as a wave and a particle (photon)

## Slide 22
Photoelectric effect
https://upload.wikimedia.org/wikipedia/commons/thumb/a/a6/Photoelectric_effect_in_a_solid_-_diagram.svg/1920px-Photoelectric_effect_in_a_solid_-_diagram.svg.png
EM radiation (photons) in, (photo)electrons out
Energy of incident EM must be above a threshold, dependent only on f
E = h * f

## Slide 23
Trivia time!
https://i2.wp.com/www.evolvedcontact.com.au/articles/wp-content/uploads/2020/04/81-817751_quiz-time-announcement-poster-neon-signboard-vector-quiz.png?fit=1024%2C417&ssl=1, https://scuffedentertainment.com/wp-content/uploads/2021/03/pub-trivia-quiz.jpg
Teams of 2–3 (card draw)
Phones and computers away

## Slide 24
Question 1 (10 mins)
https://en.wikipedia.org/wiki/Rice_cooker#/media/File:Electric_Rice_Cooker_1956.jpg
Toshiba ER-4
1956: 700 units/year
1970: 12.3M units/year
98ºC, 20 mins
Why not? And then how?

## Slide 25
Answer 1
https://m.media-amazon.com/images/I/61ZOy1oalYL._AC_SL1500_.jpg, https://upload.wikimedia.org/wikipedia/commons/thumb/c/c3/StrainGaugeVisualization.svg/1024px-StrainGaugeVisualization.svg.png
Time to reach boiling unpredictable
Time at 98ºC predicable
Bimetallic thermostat senses when the temperature of the bottom of the pan >100ºC
Senses temperature (via e-) as a proxy for time

## Slide 26
Question 2 (10 mins)
https://m.media-amazon.com/images/I/61ZOy1oalYL._AC_SL1500_.jpg
What does this actually measure?
Digital bathroom scale

## Slide 27
Answer 2
https://m.media-amazon.com/images/I/61ZOy1oalYL._AC_SL1500_.jpg, https://upload.wikimedia.org/wikipedia/commons/thumb/c/c3/StrainGaugeVisualization.svg/1024px-StrainGaugeVisualization.svg.png
A strain gauge changes electrical resistance (R) as a function of deformation
Changes in R are converted to digital units
Approach relies on calibration

## Slide 28
Concept: transducers
https://m.media-amazon.com/images/I/61ZOy1oalYL._AC_SL1500_.jpg, https://upload.wikimedia.org/wikipedia/commons/thumb/c/c3/StrainGaugeVisualization.svg/1024px-StrainGaugeVisualization.svg.png
Strain gauges are examples of transducers
Transducers convert energy from one form to another
Here: weight (kg * g) in, ∆R (V / A) out
SI base units: kg  A

## Slide 29
Question 3 (10 mins)
https://upload.wikimedia.org/wikipedia/commons/c/cb/717mpg.jpg
What does this actually measure?
Car speedometer

## Slide 30
Another conversion
https://ars.els-cdn.com/content/image/3-s2.0-B9780750651318500129-f11-40-9780750651318.gif, https://i5.walmartimages.com/asr/4fbb556a-dcde-46fe-88f7-dc4da8676bdb.736184df7fa4885998187990b6299827.jpeg
Velocity is desired readout
Angular velocity of driveshaft/axel a proxy
Velocity (m / s) in, V (Ω * A) out
SI base units: (m / s)  A
Tone wheel

## Slide 31
Answer 3
https://ars.els-cdn.com/content/image/3-s2.0-B9780750651318500129-f11-40-9780750651318.gif, https://i5.walmartimages.com/asr/4fbb556a-dcde-46fe-88f7-dc4da8676bdb.736184df7fa4885998187990b6299827.jpeg
Ferromagnetic toothed ring spins with axel or drive shaft
Sensor contains electromagnet
Teeth distort magnetic field -> creates alternating electrical field
Changes in spin speed -> changes in f of alternating V
Approach relies on calibration
Tone wheel